## Slide 1: The INTEL 80486 Microprocessor

## Slide 2: Intel 80486 (32 bit microprocessor)
In addition to the previous features, it has an additional feature, the built-in
math coprocessor
It is same as 80387 coprocessor, but being integrated on the chip allows it to execute math instructions about 3 times as fats as 386/387 combination.
8 Kbyte code & data cache
5-stage instruction pipeline scheme that allows it to execute instructions much faster than 386.

## Slide 3: Intel 80486 (32 bit microprocessor)
Example
MOV AX,MEMORY_Location
ADD CX,BX
SHR AX,1
MOV MEMORY_LOCATION,CX
Effectively , single clock cycle
4 clock cycles to execute on a 386
1 clock cycles to execute on a 486
To make room for the additional signals, the 80486 is packaged in a 168 pin, pin grid array package instead of the 132 pin PGA used for the 80386.

## Slide 4: 80486 Signal Group
The 80486 data bus, address bus, byte enable, ADS#, RDY#, INTR, RESET, NMI, M/IO#, D/C#, W/R#, LOCK#, HOLD,HLDA and BS16# signals function as we described for 80386.
The 80486 requires 1 clock instead of 2 clock required by 80386.
A new signal group on the 486 is the PARITY group DP0-DP3 and PCHK#.
These signals allow the 80486 to implement parity detection / generation for memory reads and memory writes.
During a memory write operation, the 80486 generates an even parity bit for each byte and outputs these bits on the DP0-DP3 lines.

## Slide 5: 80486 Signal Group (cont..)
These bits will store in a separate parity memory bank.
During a read operation the stored parity bits will be read from the parity memory and applied to the DP0-DP3 pins.
The 80486 checks the parities of the data bytes read and compares them with the DP0-DP3 signals. If a parity error is found, the 80486 asserts the PCHK# signal.
Another new signals group consists of the BURST ready signal BRDY# and BURST last signal BLAST#.
These signals are used to control burst-mode memory reads and writes.

## Slide 6: 80486 Signal Group (cont..)
A normal 80486 memory read operation to read a line into the cache requires 2 clock cycles. However, if a series of reads is being done from successive memory locations, the reads can be done in burst mode with only 1 clock cycle per read.
To start the process the 80486 sends out the first address and asserts the BLAST# signal high. When the external DRAM controller has the first data bus, it asserts the BRDY# signal.
In this mode the DRAM will be able to output the new data word within 1 clock cycle.

## Slide 7: 80486 Signal Group (cont..)
bus request output signal BREQ, the back-off input signal BOFF#, the HOLD signal and the hold-acknowledge signal HLDA.
These signals are used to control sharing the local 486 bus by multiple processors ( bus master).
When a master on the bus need to use the bus, it asserts its BERQ signal .

## Slide 8: 80486 Signal Group (cont..)
grant bus use to the highest – priority master. To ask the 486 to release the bus , the bus controller asserts the 486 HOLD input or BOFF# input.
If the HOLD input is asserted, the 486 will finish the current bus cycle, float its buses and assert the HLDA signal.
To prevent another master from taking over the bus during a critical operation, the 486 can assert its LOCK# or PLOCK# signal.

## Slide 9: Pentium processor
237 pins, arranged in a Pin Grid Array(PGA) package, connecting it to the external system, as compared to the 40 pins of 8086.
Data pins D0-D63
DP0-DP7,Parity of each byte of the data in the data bus
Address bus , A3-A31
Byte Enable pins, BE0-BE7
A20* pin, active low

## Slide 10: Pentium(32-bit microprocessor)
32- bit address bus
64- bit data bus
2 ALUs
2 8KB cache memories( one for code & one for data)
On-chip floating-point math coprocessor unit
Prefetch buffer
Branch-Target Buffer
Internal parity checking to detect internal parity errors.

## Slide 11: Pentium processor
486 has 5-stage pipeline
Fetch
Decode1
decode2
Data fetch from, or store to, the memory.(ALU)
Write the result
In Pentium, there are two pipelines provided for integer operation, after the decode stage.

## Slide 12
The 4MB page and Flat Memory Model
Advanced programmable Interrupt Controller(APIC)
Multimedia Extension(MMX) Technology
The INIT pin, and the Built-In-Self-Test(BIST)
Model specific Registers(MSRs)and mac hine check(MC) Exceptions
Other MSrs of the pentium processor
System management mode(SMM)