## Slide 1: Addressing Modes
• Instruction
– Op-code
– Operand
• Addressing mode indicates a way of locating data
or operands.
– Any instruction may belong to one or more addressing modes
– Some instructions may not belong to any of the addressing modes

## Slide 2: Addressing Modes
• Data-Addressing Modes
• Program Memory-Addressing Modes
• Stack Memory-Addressing Modes

## Slide 3: Addressing Modes
Immediate: The data is either 8 bits or 16 bits long and is part of the instruction
Example
– MOV AX,0001H
– MOV CX,0045H
– MOV BL,08H
– MOV AH,BFH

## Slide 4
Direct: The 16-bit effective address of the
data is part of the instruction
• Example:
– MOV AX, [5000H]
– ADD AX, [1000H]

## Slide 5
Register addressing: The data is in the register that is specified by the instruction. For a 16-bit operand, a register may be AX, BX, CX, DX,SI,DI,SP or BP. For an 8 bit operand a register may be AL, AH, BL, BH, CL, CH, DL, DH.
Example :
MOV AX,BX
ADD AL, BL

## Slide 6
Register Indirect: The effective address of the data is in the base register BX or an index register that is specified by the instruction
Example:
MOV AX, [BX]
MOV AX,[SI]

## Slide 7
Register Relative: The effective address is the sum of an 8 or 16 bit displacement and the contents of a base register or an index register