## Slide 1: The 8087 math coprocessor

## Slide 2: 8087 Data Types
3 Types
1. Binary integer
2. Packed Decimal
3. Real

## Slide 3: Binary Integers
Assembler Directive
Word integer16 bitsDW(Define Word)
Short integer 32 bitsDD(Define DoubleWord)
Long Integer 64 bitsDQ(Define Quadword)

## Slide 4: Packed Decimal Numbers
Assembler Directive
Packed Decimal80 bitsDT(Define TenBytes)

## Slide 5: Real Numbers
Assembler Directive
Short real32 bitsDD(Define DoubleWord)
Long Real 64 bitsDD(Define QuadWord)
Temporary Real 80 bitsDT(Define TenBytes)

## Slide 6: The 8087 Internal Architecture

## Slide 7: Control word format

## Slide 8: Status word format

## Slide 9: 8087 stack operation

## Slide 10: Pythagoras Theorem
Data segment word public
Side_a dd 3.0
Side_b dd 4.0
Result dd 0
Ctrl_word dw 0
Status_word dw 0
Data ends
Code segment word puplic
Assume cs: code, ds:data
Start: mov ax,data
mov ds,ax
FINIT
mov ctrl_word,03ffh
FLDCW ctrl_word
FLD side_a
FMUL ST,ST(0)
FLD side_b
FMUL ST,ST(0)
FADD St,ST(1)
FSQRT
FSTSW status_word
Mov ax,status_word
AND al,0BFH
JNZ stop
FSTP result
Stop: NOP
Code ends
End start